## Slide 7
Sr. No | Region of operation | Base emitter junction | Collector base junction | Application
1 | Cutoff region | Reverse biased | Reverse biased | Open Switch
2 | Forward active region | Forward biased | Reverse biased | Amplifier
3 | Saturation Region | Forward biased | Forward biased | Closed Switch
4 | Inverse Active | Reverse biased | Forward biased | 
Biasing conditions for different regions of operation

## Slide 11: Transistor Biasing in the Active Region:
Biasing is the process of applying external voltages to the transistor. The two junctions in a BJT must be biased properly in order to operate it as an amplifier. A transistor cannot work unless external DC power supplies are connected to it.
A BJT is capable of operating in four different regions, depending on the way in which it is biased. The regions of operation are:
1. Cutoff region (transistor is OFF)
2. Saturation region (transistor is fully ON)
3. Forward active region (in between saturation and cutoff).
4. Inverse active mode