## Slide 1: Unit 6 : Protective devices and switchgear
12marks

## Slide 2
CO: f. Use relevant protective devices/switchgear for different requirements.
Notes: f. Use relevant protective devices/switchgear for different requirements.

## Slide 3: all accessories required for wiring systems and electrical installations.
All the wiring systems and electrical installation make use of following accessories.
Cable, Flexible wires
Switches, fuses
Lamp holders, plugs
Socket outlets, junction boxes

## Slide 4: Fuse.
Fuse is a simplest device( a wire basically), which breaks the circuit under abnormal condition.
In any electrical installations, a fuse is used for protecting the appliances against overcurrent.
A fuse is basically a piece of wire which is rated to melt at a particular current. It has a low melting point.
It is used for overload/ short circuit protection.
The conducting material used for fuse are:
Copper, Zinc, Lead, Tin, Aluminium etc.

## Slide 5: Types of Fuses:
Semi enclosed or rewirable type
Totally enclosed type
Dropout type
Expulsion type
H.R.C. fuse(High Rupturing Capacity)
Striker fuse
Switch fuse

## Slide 6: MCB.
The miniature circuit breakers (MCB) have become an important part of domestic, commercial and industrial applications.
2. It is basically a tripping device which acts as a switch. Under the normal operating condition, it acts as a closed switch whereas when the current goes above a predetermined level, it acts as an open switch and breaks the circuit.
3. The MCB is available in moulded case which contains the tripping and switching mechanism.
4. The MCB is connected in series with each line of AC supply line.
5. The MCB can replace the thermal overload relay and contactor. So we don’t have to use two separate devices for protection.

## Slide 7: MCCB
MCCB is a operating switch which is use manually under normal operating condition for making ON and OFF the circuit.
2. Under fault condition it automatically trips the circuit.
3. This tripping mechanism is done by the magnetic and thermal sensing devices.
4.The tripping mechanism & terminal contacts are assembled in a moulded case therefore the name of this type is Moulded Case Circuit Breaker.

## Slide 8: ELCB
An Earth-leakage circuit breaker (ELCB) is a safety device used in electrical installations with high Earth impedance to prevent shock.
2.It detects small stray voltages on the metal enclosures of electrical equipment, and interrupts the circuit if a dangerous voltage is detected.
3.The protection against fault current or leakage current is provided by the device called Earth Leakage Circuit Breaker (ELCB).
4.Application:
ELCB is used for the domestic as well as industrial applications, to insure that the mains supply is automatically disconnected if the earth leakage current is detected. This will save the users from shocks.

## Slide 9: Earthing
Connecting the metallic frame of electrical machines, conducts pipe etc, to ground (earth) by a wire having negligible resistance is known as Earthing.

## Slide 10: Advantages of Earthing:
Earthing avoids electric shock to human body.
Earthing keeps the potential of all non current carrying conducting part to zero with respect to earth.

## Slide 11: State any two methods of Earthing.
Plate earthing & pipe earthing.
Plate Earthing: In this type of earthing plate either of copper or G.I. is buried into the ground at a depth of not less than 3m from the ground level.
Pipe Earthing: Pipe earthing is best form of earthing & it is cheap also. In this type, GI pipe of 38mm diameter & 2m long is buried vertically in ground.